## Slide 1
STA学习报告
—clarl.zhao
2025-11-24

## Slide 2: 0. 报告内容
1. introduction
2. Concepts
3. example
01
02
03
04
05
06

## Slide 3: 1. STA introduction
  Nano-meter
  What
  Why
  Design-flow
  Limitation
  Power
  Reliability

## Slide 4: 1.1 STA introduction: nano-meter
  Nano-meter：
    Shrink
    Coupling
      Noise
      crosstalk

## Slide 5: 1.2 STA introduction: what
  what：
    Simulation
      Timing & Fun
      input
    STA
      Timing only
      Statically
      No input
      statically

## Slide 6: 1.3 STA introduction: why
  why：
    Chip Failure: 80% timing violation
    STA
      complete/exhaustive (in one test):
        All path
        All scenarios
      faster/simpler
      Crosstalk and Noise
      statically

## Slide 7: 1.4 STA introduction: design-flow
  Design-flow：
    STA: sign-off
    越来越贴近真实场景
      statically

## Slide 8: 1.5 STA introduction: limitations
  limitations： scenarios than STA can’t work
    Reset sequence
      value not synthesized
    FIFO
      2 fsm for tx/rx
    Async clock domain crossings
    X-handling
    IO interface
      not possible to spec all REQs
    analog & digital Interface
    Clock synchronization logic
      医者不能自医: STA分析时钟是基准，默认时钟是idea的
    PLL settings
    Functional behavior
    False paths

## Slide 9: 1.6 STA introduction: power & Reliability
  Power
    trade off
      Cell lib
      Power
      timing
  Reliability
    Not just, but also

## Slide 10: 2. Concepts
  CMOS Logic Design
  Modeling of CMOS Cells
  Waveforms
  Delay
  Slew
  Skew
  Timing Arcs and Unateness
  Path
  Clock Domains
  Operating Conditions

## Slide 11: 2.1 CMOS Logic : COMS & inverter
  Structure
    Length
    Process
    Speed
  Inverter
    no steady current
      Dissipation:
        charge/discharge
      leakage
    capacitive load
    pull-up
    pull-down

## Slide 12: 2.1 CMOS Logic : inverter -> standard cell
  Inverter: 反相器生万物
    Logic gate
      pull-down
      pull-up
      Inv/Nand/nor/and/or
    Gate characteristic
      R
      Cap
    Standard cell
      pre-designed
      pre-characterized
        functionality
        timing
        Power
        DC transfer characters

## Slide 13: 2.2 CMOS Logic : modeling
  modeling
    Cell Out Cap
      Wire +
      fanout gate in-Cap
    Cell model
      Up/down Res : Gm
      In-Cap
    Net

## Slide 14: 2.3 waveform
  wave
    RC
    MOS gate
      短暂的到地通路
        功耗增加
        信号完整性: ir-drop/gnd-noise
        延迟

## Slide 15: 2.4 delay
  delay
    RC -> delay
    cmd
    # Threshold point of an input falling edge:
    input_threshold_pct_fall : 50.0;
    # Threshold point of an input rising edge:
    input_threshold_pct_rise : 50.0;

## Slide 16: 2.5 slew-rate
  Slew-rate
    Raise/fall
      70%/30%
      80%/20%
      90%/10%

## Slide 17: 2.6 skew
  Skew
    Between signals
    Latency
    uncertainty
      Skew
      Jitter
      margin
    Cmd
    set_clock_latency 2.2 [get_clocks BZCLK]
    set_clock_uncertainty 0.250 -setup [get_clocks BZCLK]
    set_clock_uncertainty 0.100 -hold [get_clocks BZCLK]

## Slide 18: 2.7 timing-arcs & Unateness
  Timing arcs (时序弧)
    延迟的载体
    感知逻辑关系
  Unateness (单调性)
    逻辑延迟的载体
      Positive 正相关
        and
      Nagetive 负相关
        nand
      Non-Unate 没有单调性
        Xor
        时钟处理

## Slide 19: 2.7 timing-arcs & Unateness
  逻辑感知优化
    消除悲观（避免过度保守的时序预算）
    加速分析（减少 50% 以上的无效计算）
    高阶功能
      多周期路径
      时钟门控
      数据路径平衡
    例如：
      例如：不会分析 AND 门中“A 上升导致 Z 下降
      正相关路径确保跳变类型（上升/下降）在传播过程中不发生翻转。

## Slide 20: 2.7 timing-arcs & Unateness
  example

## Slide 21: 2.8 path
  Path:
路径类型 | 起点 | 终点 | 说明
寄存器到寄存器 | Reg1/CK | Reg2/D | 最核心路径，检查时钟域内时序
输入到寄存器 | Input Port | Reg/D | 检查输入信号到达时间
寄存器到输出 | Reg/CK | Output Port | 检查输出信号有效时间
输入到输出 | Input Port | Output Port | 纯组合路径，检查总延迟
set_input_delay -clock CLK [get_ports A] # 定义输入路径起点set_output_delay -clock CLK [get_ports Z] # 定义输出路径终点

## Slide 22: 2.8 CMOS Logic : path
  path
    STA分析的主体
    Max : late path
    Min : early path
    Reg to Reg path
      Launch: uff1/uff2
      Capture: uff3

## Slide 23: 2.9 CLK domain
  CLK domain
    flip-flops fed by same clk
    CDC before STA
  Not fed the same clk
    independent
    Related
      Real path
      False path
      双向独立约束
  RISK
    将真实路径误设为false path
      硅片静默失效
    未设 multicycle
      过度优化
        功耗面积浪费
    约束方向错误
      -start/-end混淆
        时序窗口计算错误

## Slide 24: 2.9 CLK domain：real-path example
Checklist:
1. 同步分频/倍频路径
  设置 multi-cycle
2. 握手控制信号路径
  setup检查仍必须满足最小脉冲宽度
3.异步FIFO指针同步路径（严格设计）
  设max_delay确保指针变化远离采样边沿
  更精确的set_data_check
4.门控/派生时钟的使能路径
  设max_delay 确保使能信号在时钟有效边沿前稳定
5.复位同步释放路径
  恢复时间（Recovery)
  移除时间（Removal）
6.时钟切换/复用路径（Clock Muxing）
  set_clock_groups :physically_exclusive
7.电源域交叉路径（Isolation Cells）
  set_isolation_control
8.相位偏移时钟路径（Phase-Shifted PLL）
  默认单周期约束误吞相位差导致setup违例
9.源同步接口（Source Synchronous）ddr/serdes
  set_bus_skew
  data_check
10，... 永远不可能完备

## Slide 25: 2.9 CLK domain：real-path checklist
Checklist:
  Universal 必须
    执行report_clock_interaction → 无"Timed (Unsafe)"标记
    执行report_exceptions -ignored → 无非预期忽略的时序弧
    所有 async_set/reset → 已设false_path但保留recovery/removal
  Design-Pattern Based 模式匹配
    存在分频器：检查multicycle_path -setup与-hold是否成对
    存在FIFO：检查格雷码路径max_delay < 目标时钟周期/2
    存在时钟切换：检查clock_groups是否设为physically_exclusive
    存在电源域：检查isolation_cell时序约束覆盖率100%
    存在源同步接口：检查bus_skew vs data_check 约束
  Project-Specific 项目定制
    动态调频设计：operating_conditions是否覆盖所有频点组合
    低功耗设计：retention_cell的save/restore时序约束
    安全岛设计：lockstep比较器路径的max_delay约束

## Slide 26: 2.9 CLK domain：operation condition
PVT
  for STA
    Worst-Case Slow
      Process is slow
      temperature is highest or lowest
        温度↓ ；晶格振动↓；迁移率↑；dly↓
        <65nm：t↓；Vth ↑; dly ↑
      and voltage is lowest
    Typical
    Best-Case Fast
      Process is fast
      temperature is lowest
      and voltage is highest
  for power analysis
    Maximal Leakage
      Process is fast
      temperature is highest
      voltage is also the highest
    Typical Leakage
      Process is typical
      temperature is highest 因为芯片运行起来，就会接近最高温度...
      voltage is nominal

## Slide 27: 3 STA : set & hold
setup
  why need : RC
  path-type: max 所有的延迟，都要用最大值来计算
  前/后沿检查
hold
  why need : DFF = 2 master & slave latch
  path-type: min 所有的延迟，要用最小值来计算
  同一个沿检查

## Slide 28: 3.1 SET：reg_to_reg
Tlaunch + Tck2q +Tdp < Tcapture + Tcycle – Tsetup
  Tlaunch – Tcapture = skew
  Tcycle -> expect-freq
  Tck2q, Tsetup -> standard cell
  Tdp is Target
  工具会报slack
If violate :
  Skew
  Freq ↓
  Tdp 拆分

## Slide 29: 3.1 SET：inverter & dff
Inverter - > 2*n = delay cell
  Delay
  Skew
DFF -> 打一拍
  Tdp 拆分，拆分组合逻辑
    MIPS 5级流水线

## Slide 30: 3.2 hold：reg_to_reg
Tlaunch + Tck2q + Tdp > Tcapture + Thold
  Tlaunch – Tcapture = clk skew
  Tck2q, Thold -> standard cell
  Tdp is Target
  has no effect with freq
If violate :
  Tdp 加逻辑/换慢cell
  Skew 要谨慎
    先set；再hold

## Slide 31: 3.3 multi-cycle
如果某段电路 Tdp 一个cycle的确搞不定
  可以约束为multi-cycle
  时序关系不是那么严苛
  Set :n cycle 绝对 / hold: (n-1) cycle 相对
场景类型 | 典型电路 | 多周期数 | Setup/Hold约束 | 风险等级
分频时钟域 | 时钟分频器 | 2/4/8周期 | N-1, N-2 | 低
低速数据处理 | 复杂算术单元 | 2-5周期 | N-1 | 中
数据同步 | 握手协议、FIFO指针 | 2周期 | 0, -1 | 中
时钟使能逻辑 | 门控使能信号 | 2-4周期 | N-1 | 高（易出错）
移位寄存器链 | 长移位寄存器 | 长度-1 | 0 | 低
跨时钟域同步 | 同步器链 | ≥2周期 | 0 | 极低（建议false path）

## Slide 32: 3.4 half-cycle
如果时钟路径中，有一个反相器
  Hold时间很友好，加了半周期
  Set 时间上面的公式就变成了 Tcycle/2; 变难了
STA :
  cmd要特别说明
Case：
场景 | 是否推荐 | 约束复杂度 | 风险等级
DDR接口 | ✅ 必需 | 低（工具自动） | 低
时钟反相 | ⚠️ 避免 | 中 | 中
占空比失真 | ❌ 禁止 | 高 | 高
故意半周期逻辑 | ❌ 绝对禁止 | 极高 | 极高

## Slide 33: 汇报完毕
  谢谢观看~！